## Slide 1: STUN, TURN and ICE
Cary Fitzgerald

## Slide 2: Simple Traversal of UDP Through NAT (STUN)
RFC 3489
Works with Existing NAT
Main Features
  Allows Client to Discover Presence of NAT
  Works in Multi-NAT Environments
  Allows Client to Discover Type of NAT
    Symmetric
    Full Cone
    Restricted Cone
    Port Restricted Cone
  Allows Discovery of Binding Lifetimes
  Allows Clients to Discover if They are in the Same Address Realm
  Stateless Servers

## Slide 3: How Does it Work?
Basic Operation
  Client Sends a Request to STUN Server
    Can be Discovered Through DNS
  STUN Server Copies Source Address into Response
Additional Capabilities
  Server Signs the Response
  Server Sends Response from Different Socket
  Server Sends Response to Different Socket
Client Uses Server to Perform Different Functions
  NAT Discovery
  Binding Discovery
  Lifetime Discovery
Client
STUN
Server
N
A
T
N
A
T
Whats my IP?
1.2.3.4:8877
NAT rewrites
Source to 1.2.3.4:8877
10.0.1.1:6554

## Slide 4: Binding Acquisition
Client sends STUN Request to Server
  STUN Server can be ANYWHERE on Public Internet
STUN Server Response
Client knows Public IP for that Socket
Client Sends INVITE Using that IP to Receive Media
Call Flow Proceeds Normally
  No Special Proxy Functions
Media Flows End-To-End
STUN
STUN Request
STUN
Response
1.2.3.4:8866
INVITE
1.2.3.4:8866
200 OK
ACK
RTP

## Slide 5: NAT Type Determination
+--------+
| Test |
| I |
+--------+
|
|
V
/\ /\
N / \ Y / \ Y +--------+
UDP <-------/Resp\---------->/ IP \------------>| Test |
Blocked \ ? / \Same/ | II |
\ / \? / +--------+
\/ \/ |
| N |
| V
V /\
+--------+ Sym. N / \
| Test | UDP <---/Resp\
| II | Firewall \ ? /
+--------+ \ /
| \/
V |Y
/\ /\ |
Symmetric N / \ +--------+ N / \ V
NAT <--- / IP \<-----| Test |<--- /Resp\ Open
\Same/ | I | \ ? / Internet
\? / +--------+ \ /
\/ \/
| |Y
| |
| V
| Full
| Cone
V /\
+--------+ / \ Y
| Test |------>/Resp\---->Restricted
| III | \ ? /
+--------+ \ /
\/
|N
| Port
+------>Restricted

## Slide 6: STUN Pros and Cons
Benefits
  No Changes Required in NAT
  No Changes Required in Proxy
  Works Through Most Residential NAT
  Works Through NAT Tandem
    MIDCOM Can’t Work Here
  End-to-End Media Flows
    Low Latency
    Higher QoS
  Robust STUN Servers
  Works for Many Applications
    VoIP
    Games
    File Sharing
Drawbacks
  Doesn’t Allow VoIP To Work Through Symmetric NAT
    Typical in Large Enterprise
  RTCP May Not Work
  Need to Keep Media Flowing to Keep Bindings Alive
  May not work if both sides are behind same NAT

## Slide 7: TURN Overview
STUN doesn’t work
  through symmetric NAT
  Sometimes when clients behind the same NAT
TURN addresses these cases
Works similar to STUN
  Client sends IP/port request to TURN server
  TURN server provides one that is a local interface
  TURN server receives media on that IP/port
    Forward it to IP/port where TURN request came from
    Will get routed back to client
Client
TURN
Server
N
A
T
N
A
T
Give me IP
8.7.6.9:3884
NAT rewrites
Source to 1.2.3.4:8877
10.0.1.1:6554
RTP to
8.7.6.9:3884
RTP to
1.2.3.4:8877

## Slide 8: TURN Details
Media flows through TURN Server
  Not the case with STUN servers
  Increases voice latency
  Increases probability of packet loss
TURN provides primitives for allocating and freeing address
TURN has more extensive security requirements
  Allocates resources, STUN does not
TURN can also provide TCP connectivity
TURN works with all NAT types

## Slide 9: ICE Problem Statement
There are Many Documented Solutions for NAT Traversal for SIP
  STUN
  TURN
  B2BUA with media
  Symmetric RTP
All of Them Have a Sweet Spot of Operation, but None of Them are Ideal in All Scenarios
  Too expensive
  Too complex
Problem
  Need a SINGLE algorithm that can be placed into client devices which will
    Work in all scenarios
    Be a good solution in all scenarios
    Not require configuration or knowledge of network topology

## Slide 10: Solution: Interactive Connectivity Establishment (ICE)
Working Item of the mmusic Working Group in IETF
ICE Is a Methodology for NAT Traversal
  Makes use of STUN, TURN, RSIP, MIDCOM
  Primarily resident within the clients
ICE Explains How to Use the Other Protocols for NAT Traversal
ICE Properties
  Always will find a means for communicating if one physically exists
  Always finds the communications path with fewest relays
  Always finds the communication path cheapest for the service provider
  Does not require any knowledge of topology, NAT types, or anything
  Can guarantee that the phone won’t ring unless audio works when you pick up

## Slide 11: ICE Key Concepts
A Client Has Many Addresses at Which It Can Receive Media
  Local interfaces
  VPN Interfaces
  IP Addresses learned from STUN
  IP Addresses learned from TURN
Which One(s) Will Work When Talking to a Specific Peer?
  NO WAY TO KNOW AHEAD OF TIME
ICE Says: Try Each of Them
  Each side uses a “connectivity check” to see if It can reach a specific address provided by the peer
  These checks are done using a peer to peer STUN configuration
Choose The Highest Priority Address That Works

## Slide 12
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
X:Y

## Slide 13
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
Caller gets STUN
And TURN addresses
From server STUN: A:B
TURN: C:D
X:Y

## Slide 14
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
INVITE
O=IN IP4 C
M=audio D RTP/AVP 0
A=candidate: UDP A:B
A=candidate: UDP C:D
A=candidate: UDP X:Y
STUN: A:B
TURN: C:D
Local: X:Y

## Slide 15
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
Callee gets STUN
And TURN addresses
From server STUN: E:F
TURN: G:H
U:V
STUN: A:B
TURN: C:D
Local: X:Y

## Slide 16
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
200 OK
O=IN IP4 G
M=audio H RTP/AVP 0
A=candidate: UDP E:F
A=candidate: UDP G:H
A=candidate: UDP U:V
STUN: E:F
TURN: G:H
Local: U:V
STUN: A:B
TURN: C:D
Local: X:Y

## Slide 17
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
STUN: E:F
TURN: G:H
Local: U:V
STUN: A:B
TURN: C:D
Local: X:Y
Media starts flowing immediately to the c/m value of the peer
U:V
C:D
X:Y
G:H

## Slide 18
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
STUN: E:F
TURN: G:H
Local: U:V
STUN: A:B
TURN: C:D
Local: X:Y
Connectivity checks
Ensue from callee to caller STUN and TURN ones work
Same in reverse (not shown)
U:V
C:D
X:Y
A:B
X:Y

## Slide 19
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
INVITE
O=IN IP4 A
M=audio B RTP/AVP 0
A=candidate: UDP A:B
A=candidate: UDP C:D
A=candidate: UDP X:Y
STUN: A:B
TURN: C:D
Local: X:Y

## Slide 20
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
200 OK
O=IN IP4 E
M=audio F RTP/AVP 0
A=candidate: UDP E:F
A=candidate: UDP G:H
A=candidate: UDP U:V
STUN: E:F
TURN: G:H
Local: U:V
STUN: A:B
TURN: C:D
Local: X:Y

## Slide 21
Caller
Callee
NAT
NAT
TURN/
STUN
TURN/
STUN
Proxy
Proxy
STUN: E:F
TURN: G:H
Local: U:V
STUN: A:B
TURN: C:D
Local: X:Y
Media starts flowing to the c/m value of the peer
U:V
X:Y
A:B
E:F